DOE – 002 – Range Drift

This experiment is to determine the amount of drift due to range and to determine if there is a min / max or optimal range.

Setup:

- Black body source powered up and at temperature for 1 hour @ 37C
- Camera Powered up for 1 hour.
- Camera placed on tripod and aimed at source at close distance, measure distance to black body. Record raw pixel value.
- Repeatedly move camera further away from source, measure distance and record raw pixel values.